## Slide 1
ECE 298A TERM PROJECT PROPOSAL
A charge-pump PLL on Tiny Tapeout GF180
ECE 298A · Charge-pump PLL · Ihsan Salari, Dhyey Bhatt
1 / 3
Statement of purpose
Build a classic charge-pump phase-locked loop: a clock multiplier, the standard circuit every chip uses to make a fast clock from a slow one.
It multiplies a 5 to 12.5 MHz reference by 8N (N = 1 to 5) onto a 50 to 200 MHz on-chip oscillator.
Mixed-signal by design: the phase detector and dividers are standard-cell logic, and the charge pump, loop filter and VCO are transistor-level analog.
It exercises the whole open-source flow: RTL and CocoTB, ngspice across corners, layout with DRC and LVS.
System diagram
Reference
clk pin
5 to 12.5 MHz
PFD
phase-frequency
detector
Charge pump
UP, DN in
Icp out
Loop filter
R + C1, shunt C2
Vctrl on ua[0]
Lock detect
UP, DN width
uo_out[2]
Divider
÷N, N = 1 to 5
uo_out[1]
VCO
starved ring
50 to 200 MHz
Prescaler
÷8 toggle flops
uo_out[0]
Vctrl
feedback
digital (standard cells)
analog (transistor level)
pin
lock check

## Slide 2
INTERFACE AND TARGETS
Pin assignment and proposed specification
ECE 298A · Charge-pump PLL · Ihsan Salari, Dhyey Bhatt
2 / 3
IO pin assignment (Tiny Tapeout analog tile)
Pin | Dir | Use
clk | in | reference, 5 to 12.5 MHz
rst_n, ena | in | standard reset and enable
ui_in[2:0] | in | N, the divide ratio (1 to 5)
ui_in[5:3] | in | spare
ui_in[6] | in | PLL enable (powers down pump, VCO)
ui_in[7] | in | observe VCO ÷8 or ÷16
uo_out[0] | out | VCO ÷8 or ÷16
uo_out[1] | out | feedback divider output
uo_out[2] | out | lock
uo_out[4:3] | out | UP, DN (debug)
uo_out[7:5] | out | spare, driven low
uio[1:0] | in | charge-pump current trim
uio[7:2] | in | spare
ua[0] | analog | Vctrl, the loop-filter node
ua[1] | analog | bias reference (external resistor)
Proposed specification
Parameter | Target
Reference | 5 to 12.5 MHz (nominal 6.25 MHz)
Multiplication | 8N with N = 1 to 5, so 8× to 40×
Nominal output | 6.25 MHz × 16 = 100 MHz
VCO range | 50 to 200 MHz, typical corner
Prescaler | fixed ÷8, so all logic runs ≤ 50 MHz
Charge pump | Icp ≈ 20 µA, 2-bit trim
Loop filter | R ≈ 26 kΩ, C1 ≈ 20 pF, C2 ≈ C1/10
Phase margin | ≥ 45° at N = 2 (8N = 16)
Lock time | under 50 µs
Observed output | VCO ÷8 or ÷16 on uo_out[0]
First ngspice runs at the typical corner: Icp 19 µA, VCO 10 to 258 MHz, phase margin 49.5° at 8N = 16.

## Slide 3
PLAN
Timeline for completion and who does what
ECE 298A · Charge-pump PLL · Ihsan Salari, Dhyey Bhatt
3 / 3
Timeline for completion
Oct 8
Digital RTL (PFD, prescaler, divider, lock detector) and a loop model, CocoTB passing; first pump and VCO schematics
Nov 5
Evaluation: pump, filter and VCO across ngspice corners; the full loop locks in simulation; loop values fixed
Nov 26
System verification: layout DRC and LVS clean, post-layout re-simulation, Tiny Tapeout precheck green
Dec 3
Documentation and a silicon test plan
Who does what
Ihsan Salari
ANALOG
Charge pump, loop filter and VCO
ngspice corner sweeps
Analog layout, DRC and LVS
Dhyey Bhatt
DIGITAL
PFD, prescaler, divider, lock detector
CocoTB testbench and loop model
Synthesis and timing
Both
TOGETHER
Top-level integration and full-loop simulation
Documentation, GitHub and presentations